Guide for System Center 2012 Monitoring Pack for Remote Access

Microsoft Corporation

Published: July 2012

Send suggestions and comments about this document to mpgfeed@microsoft.com. Please include the monitoring pack guide name with your feedback.

We encourage you to provide feedback on the management pack by providing a review on the management pack’s page in the Management Pack Catalog (http://go.microsoft.com/fwlink/?LinkID=82105).

Copyright

This document is provided "as-is". Information and views expressed in this document, including URL and other Internet Web site references, may change without notice. You bear the risk of using it.

Some examples depicted herein are provided for illustration only and are fictitious.  No real association or connection is intended or should be inferred.

This document does not provide you with any legal rights to any intellectual property in any Microsoft product. You may copy and use this document for your internal, reference purposes. You may modify this document for your internal, reference purposes.

© 2011 Microsoft Corporation. All rights reserved.

Microsoft, Active Directory, Windows, and Windows Server are trademarks of the Microsoft group of companies.

All other trademarks are property of their respective owners.

Abstract

Microsoft System Center Monitoring Pack for Remote Access helps you monitor the health and availability of computers configured for Remote Access server role and running Windows Server 2012. This guide describes how to install the System Center Monitoring Pack for Remote Access in Microsoft® System Center Operations Manager 2012(Operations Manager 2012).

The information that is contained in this document represents the current view of Microsoft Corporation on the issues discussed as of the date of publication. Because Microsoft must respond to changing market conditions, it should not be interpreted to be a commitment on the part of Microsoft, and Microsoft cannot guarantee the accuracy of any information presented after the date of publication.

Contents

Guide for System Center Monitoring Pack for Remote Access	7

Guide History	7

Supported Configurations	7

Files in this Monitoring Pack	7

Monitoring Pack Purpose	7

What’s New	8

DirectAccess Monitoring	8

VPN Monitoring	8

Getting the Latest Management Pack and Documentation	10

How to Import the Routing and Remote Access Service Management Pack	10

Create a New Management Pack for Customizations	10

Security Considerations	11

Discovered Objects	11

How Health Rolls Up	12

Monitoring Scenarios	14

DirectAccess Monitoring Scenarios	14

RRAS Monitoring	19

VPN Monitors and Alarms	27

Performance Monitoring Scenarios	29

Event Monitoring Scenarios	30

Tasks	35

# Guide for System Center Monitoring Pack for Remote Access

This guide was written based on version 7.0.8560.0 of the Monitoring pack for Microsoft System Center 2012 Remote Access

## Guide History

| Release Date | Changes |
| --- | --- |
| September 2012 | Original release of this guide |

## Supported Configurations

This management pack requires System Center Operations Manager 2012 or later.

The following table details the supported configurations for the Monitoring pack for Remote Access:

| Configuration | Support |
| --- | --- |
| Windows Server 2012 Remote Access | Yes |
| Windows Server 2008 R2 | Not supported |

## Files in this Monitoring Pack

The Monitoring Pack includes the following files:

	License Agreement

	Microsoft.Windows.RemoteAccess.2012.Monitoring.mp

## Monitoring Pack Purpose

The System Center Monitoring Pack for Remote Access helps you monitor the health and availability of the unified Remote Access Server role on computers running Windows Server 2012.

This guide describes how to install the System Center Monitoring Pack for Remote Access in Microsoft® System Center Operations Manager 2012 (Operations Manager 2012).

The management pack provides a predefined, ready-to-run set of processing rules, alarms, monitors, and performance instrumentation that are designed to monitor the Remote Access service components. This management pack primarily monitors two components – DirectAccess and RRAS. DirectAccess health is monitored by executing the powershell based RemoteAccess Health commandlets. RRAS is monitored via events that are placed in the Application and System event logs by various RRAS components and subsystems.

This guide provides information about the most common monitoring scenarios, monitor definitions, tasks, and views for Remote Access. This guide also includes instructions for deploying and operating the management pack.

## What’s New

System Center Monitoring Pack for Remote Access combines monitoring for DirectAccess and RRAS into a single management pack. Monitoring capabilities for DirectAccess have been enhanced to cover more components and encompass larger set of health scenarios. This management pack monitors the following conditions:

### DirectAccess Monitoring

- Issues with internal and external network adapter connection and settings such as forwarding

- Teredo server state and configuration

- Isatap availability and configuration such as name publishing and route publishing

- 6to4 adapter and forwarding state

- Heuristics around network security such as DOS attack, spoof attack and replay attack and state of IPSec

- State of network infrastructure like Dns servers, Management servers configured for DirectAccess

- IP-Https state and configuration

- State of various underlying services such as BFE, IPHelper etc needed for Remote Access

- Heuristics related to OTP

Most of the health monitoring scenarios that can be monitored using the native DirectAccess UI have been included in the management pack.

### VPN Monitoring

Existing capabilities for RRAS management pack have been included in the unified management pack as well. We’ll summarize the monitoring capabilities for RRAS included in the unified management pack:

	Remote access (VPN) connection failures due to erroneous configuration.

	Demand-dial (site-to-site) connection failures due to erroneous configuration.

	Erroneous configuration of VPN tunnels:

	Point-to-Point Tunneling Protocol (PPTP)

	Layer Two Tunneling Protocol (L2TP/IPSec)

	Secure Socket Tunneling Protocol (SSTP)

	Internet Key Exchange version 2 (IKEv2)

	Connection licenses, registry corruption, authentication, and accounting issues for remote access

	VPN network access protection (NAP) enforcement and Network Access Quarantine Control access issues

	Erroneous configuration and setup issues involved with various routing protocols that are exposed through RRAS, such as the following:

	Routing Information Protocol (RIP) v1 and v2

	DHCP Relay Agent

	Internet Group Management Protocol (IGMP)

	DHCPv6 Relay Agent

- Monitors and alarms to notify the administrator about erroneous conditions. These conditions include the following:

	Hardware device error

	Protocol initialization failure

	Remote Access Connection Manager (RASMAN) service unexpected termination

	Routing and Remote Access service unexpected termination

	Routing and Remote Access service monitor

	Authentication or accounting failures

	Configuration failures

	IPsec-related failures

	Packet filter-related failure

	IPCP negotiation failure

	Memory allocation monitor

	Memory allocation failure

	No more licenses monitor

	Port open failures

- Support for monitoring performance counters and instrumentation, including the following:

	Total number of remote access connections

	Total number of timeout and serial overrun errors for this connection

	Total number of alignment errors for this connection (alignment errors occur when a byte received is different from the byte expected)

	Total number of buffer overrun errors for this connection (buffer overrun errors occur when the software cannot handle the rate at which data is received)

	Total number of bytes received for this connection

	Number of bytes received per second

	Total number of bytes transmitted for this connection

	Number of bytes transmitted per second

	Total number of cyclic redundancy check (CRC) errors for this connection (CRC errors occur when the frame received contains erroneous data)

	Total number of data frames received for this connection

	Number of frames received per second.

## Getting the Latest Management Pack and Documentation

You can find the System Center Monitoring Pack for Remote Access in the System Center Operations Manager Marketplace.

## How to Import the Routing and Remote Access Service Management Pack

For instructions about importing a management pack, se How to Import a Management Pack in Operations Manager 2012 (http://technet.microsoft.com/en-us/library/hh212691.aspx).

## Create a New Management Pack for Customizations

Most vendor management packs are sealed so that you cannot change any of the original settings in the management pack file. However, you can create customizations, such as overriding a default behavior or creating new monitoring objects, and then save them to a different management pack. By default, Operations Manager 2012 saves all customizations to the default management pack. As a best practice, you should instead create a separate management pack for each sealed management pack that you want to customize.

Creating a new management pack for storing overrides has the following advantages:

	It simplifies the process of exporting customizations that were created in your test and preproduction environments to your production environment. For example, instead of exporting a default management pack that contains customizations from multiple management packs, you can export just the management pack that contains customizations of a single management pack.

	You can delete the original management pack without needing to first delete the default management pack. A management pack that contains customizations is dependent on the original management pack. This dependency requires that you delete the management pack with customizations before you can delete the original management pack. If all of your customizations are saved to the default management pack, you must delete the default management pack before you can delete an original management pack.

	It’s easier to track and update customizations to individual management packs.

For more information refer to Creating a Management Pack for Overrides (http://technet.microsoft.com/en-us/library/hh212841.

## Security Considerations

You may need to customize your management pack. The management pack will try to execute the following commandlets on the monitored servers

- Get-RemoteAccess

- Get-DAMultisite

- Get-RemoteAccessHealth

The ‘Run As Account’ configured needs to have read permissions for the DirectAccess Server GPO.  The configured account also needs the local admin permissions on all the Remote Access Servers. It is highly recommended that you use a separate security group for the accounts configured for Operations Manager 2012.

## Discovered Objects

The Remote Access Management Pack discovers the object types described in the following table.

For information about discovering objects, see Understanding Classes and Objects in System Center 2012. (http://technet.microsoft.com/en-us/library/hh457568) in Operations Manager 2012 Help.

| Category | Object Type | Discovered Automatically |
| --- | --- | --- |
| Remote Access Server Seed Discovery | Windows Server 2012 | Yes (every 5 hours) |
| Remote Access Server Powershell based component discovery | Remote Access Site Remote Access Server VPN Server DirectAccess Server Teredo 6to4 DNS DNS64 Domain Controller IPSec Management Servers NAT64 Network Adapters Network Location Server Network Security Services ISATAP Kerberos Otp High Availability | Yes (every 6 hours) |

## How Health Rolls Up

The class hierarchy for System Center Monitoring Pack for Remote Access is shown below. The blue arrows show the hierarchy while red dotted ones show health rollup.

Health Monitors are targeted to all leaf node classes of the above hierarchy. Health is rolled up along the red arrows marked above. Health is rolled up in all four categories namely

- Configuration

- Availability

- Performance

- Security

## Monitoring Scenarios

Monitoring scenarios for Remote Access Server can be broken down into monitoring of two main components:

- DirectAccess monitoring

- RRAS monitoring

### DirectAccess Monitoring Scenarios

| Monitor | Description |
| --- | --- |
| Corporate network route publish | DirectAccess clients cannot connect to all resources on the corporate network. |
| Network adapter state | The network adapters are either disconnected or disabled. |
| External adapter forwarding state | Forwarding is not enabled on the external adapter. |
| Internal adapter forwarding state | Forwarding is disabled on the internal network adapter. This might prevent remote clients from accessing internal network resources. |
| Teredo Server - IP Helper service state | The IP Helper service (iphlpsvc) has stopped. DirectAccess might not function as expected. The IP Helper service provides tunnel connectivity using the connectivity platform, IPv6 transition technologies, and IP-HTTPS. |
| Teredo Server IP address validity | The Teredo server primary or secondary IPv4 addresses are invalid. |
| Teredo Server state | The Teredo server has stopped. |
| Teredo Server initialization state | The Teredo server cannot be started. |
| Teredo Server Forwarding | Forwarding is disabled on the Teredo server. |
| ISATAP Adapter availability | ISATAP adapter is not available. |
| ISATAP Route advertisement state | Route advertising is disabled on the ISATAP router. |
| ISATAP route publish | The ISATAP route is not published. |
| ISATAP Adapter forwarding state | Forwarding is disabled on the ISATAP adapter. |
| ISATAP Hostname publish state | The ISATAP server name cannot be resolved. |
| ISATAP Server - IP Helper service state | The IP Helper service (iphlpsvc) has stopped, and DirectAccess might not work as expected. The IP Helper service provides tunnel connectivity using the connectivity platform, IPv6 transition technologies, and IP-HTTPS. |
| 6to4 Adapter state | 6to4 interface is not working on the Remote Access server. |
| 6to4 Forwarding state | Forwarding is disabled on the 6to4 adapter. |
| 6to4 IP Helper service state | The IP Helper service (iphlpsvc) has stopped, and DirectAccess might not work as expected. The IP Helper service provides tunnel connectivity using the connectivity platform, IPv6 transition technologies, and IP-HTTPS. |
| Base Filtering Engine service state | Network security is not working as expected. The Base Filtering Engine (BFE) service has either been stopped, or is not responding.BFE is a service that manages firewall and IPsec policies, and implements user mode filtering. Disabling the BFE service reduces system security, and IPsec management and firewall applications might not work as expected. |
| IKEEXT service state | Network security is not working as expected. The IKE and AuthIP IPsec Keying Modules (IKEEXT) service was stopped, or is not responding. |
| IPsec-DoSP state | IPsec Denial of Service Protection (DoSP) is not enabled. |
| Potential DoS attack | A Denial of Service (DoS) attack might be underway. |
| Potential DoS attack (MM) | A Denial of Service (DoS) attack might be underway. IPv6 Main Mode negotiation failures have reached warning or critical levels. |
| Potential spoofing attack | A network security component is under a spoofing attack. |
| Potential replay attack | A network security component is under a Replay attack. A Replay attack is a form of network attack in which a valid data transmission is maliciously or fraudulently repeated or delayed. |
| Inbound Rate Limit Discarded ICMPv6 Packets/Sec | Network Security ICMP Queue Overflow Warning. |
| Inbound Rate Limit Discarded IPv6 IPsec Authenticated Packets/sec | Network Security Queue Overflow Warning |
| Inbound Rate Limit Discarded IPv6 IPsec UnAuthenticated Packets/sec | The Inbound Rate Limit Discarded IPv6 IPsec Unauthenticated Packets/sec counter has exceeded a defined threshold. View this counter under IPsec DOS Protection in Performance Monitor. This counter defines the rate at which unauthenticated IKEv1, IKEv2, AuthIP, or ESP IPv6 packets received on a public adapter were discarded because they exceeded the rate limit for IPv6 IPsec unauthenticated packets per second. An unauthenticated packet is an IPsec packet without an associated state entry. A state entry is a pair of IPv6 addresses that is authorized to pass through from a public to an internal adapter. |
| Current State Entries | The Current State Entries counter has exceeded critical levels. View this counter under IPsec DOS Protection in Performance Monitor. This counter defines the number of active state entries in the table. A state entry is a pair of IPv6 addresses that is authorized to pass through from a public to an internal adapter. |
| DNS Server availability | One or more enterprise DNS servers used by DirectAccess clients for name resolution are not available. |
| DNS Server responsiveness | Enterprise DNS servers used by DirectAccess clients for name resolution are not responding. This might affect DirectAccess client connectivity to corporate resources. |
| DNS Server responsiveness | None of the enterprise DNS servers used by DirectAccess clients for name resolution are responding. This might affect DirectAccess client connectivity to corporate resources. |
| IPHTTPS Forwarding state | Forwarding is disabled on the IP-HTTPS adapter. |
| IPHTTPS Route advertisement state | Route advertisement is disabled on the IP-HTTPS adapter. |
| IPHTTPS Route publish | The IP-HTTPS route does not have published property enabled |
| IPHTTPS Listener state | The IP-HTTPS listener is inactive and cannot accept connections from DirectAccess clients. |
| IPHTTPS Certificate validity | The IP-HTTPS certificate is not valid. |
| IPHTTPS Certificate availability | The IP-HTTPS certificate is missing. |
| IPHTTPS Certificate binding | The certificate binding to HTTPS port 443 has changed. This certificate is used for IP-HTTPS authentication.Without the correct certificate, clients cannot connect. |
| IPHTTPS – VPN SSTP Certificate not same | The specified IP-HTTPS certificate is different from the VPN SSTP certificate. IP-HTTPS and SSTP must use the same certificate because both use port 443. |
| IPHTTPS - IP Helper service state | The IP Helper service (iphlpsvc) has stopped. DirectAccess might not function as expected. The IP Helper service provides tunnel connectivity using the connectivity platform, IPv6 transition technologies, and IP-HTTPS. |
| IPSec Port or protocol blocked | Ports or protocols blocked on the internal or external network adapters are preventing Remote Access from functioning as expected. |
| IPSec Certificate validity | The certificate used for IPsec authentication is not valid. |
| IPSec Root certificate availability | The certificate used for IPsec authentication is missing. |
| IPsec certificate availability | There is no valid certificate to be used by IPsec which chains to the root/intermediate certificate configured to be used by IPsec in the DirectAccess configuration. |
| KDC Proxy Server (kpssvc) service state | A network authentication service (kpssvc) is not available. This service helps in authenticating DirectAccess clients when they connect to thecorporate network via DirectAccess. |
| Kerberos authentication | Ports required for Kerberos authentication are blocked. Kerberos authentication is required to authenticate clients using Kerberos proxy on this server. For clients to communicate with the proxy, firewalls must allow HTTPS traffic (port 443 by default). The Kerberos proxy must be able to send Kerberos authentication protocol traffic via port 88, and Kerberos change password protocol traffic via port 464 to domain controllers. |
| Kerberos Certificate validity | The certificate used for Kerberos authentication is not valid. |
| Missing Kerberos certificate | The certificate used for Kerberos authentication is missing. |
| Kerberos certificate binding | The certificate binding for HTTPS Port 443 has changed. This certificate is used to authenticate remote clients with Kerberos. Without the correct certificate, authentication of remote clients connecting via DirectAccess will not work as expected. |
| DC Server availability | The corporate domain controller for is not available. |
| NLS Server availability | The network location server is unavailable or not responding. This might disrupt DirectAccess connectivity, and connectivity for DirectAccess clients located inside the corporate network. |
| NLS URL availability | There is no response from the network location server URL. DirectAccess connectivity might not work as expected, and DirectAccess clients located inside the corporate network might not be able to reach internal resources |
| Network location server resolution state | The network location server does not have a valid DNS entry. DirectAccess clients located in the corporate network will not be able to resolve the server name, and internal network connectivity will not work as expected. |
| NLS Certificate validity | The network location server certificate is not valid. Connectivity for DirectAccess clients located in the internal network will not work as expected. |
| NLS Certificate availablity | The certificate configured for the network location server cannot be found. DirectAccess clients located in the corporate network might experience connectivity issues. |
| NLS Certificate binding | The certificate binding for the network location server has been modified. Without the correct certificate, connectivity for DirectAccess clients located in the internal network will not work as expected. |
| Management Server availability | One or more management servers are unavailable or not responding. Updates required for corporate compliance of DirectAccess client computers might not work as expected. |
| All Management servers availability | All management servers are unavailable or not responding. Updates required for DirectAccess client compliance might not work as expected. |
| DNS64 Server state | DNS64 is disabled on the server. DNS64 provides access to IPv4-only servers in the corporate network. |
| DNS64 resolution | DNS name resolution for IPv4 servers failed. DirectAccess clients might not be able to access IPv4-only servers in the corporate network. |
| DNS64 translation | DNS name resolution for IPv4 servers failed. DirectAccess clients might not be able to access IPv4-only servers in the corporate network. |
| NAT64 Server state | NAT64 is disabled on the server. NAT64 is used to provide access to IPv4-only servers in the corporate network. |
| NAT64 connection | NAT64 connectivity failed. DirectAccess clients might not be able to access IPv4-only servers in the corporate network. |
| NAT64 translation failure | NAT64 translation failures might be preventing remote clients from accessing IPv4-only servers in the corporate network. |
| Remote Access Services state | System services required for the server to function properly are not running. |
| RemoteAccess Server configuration state | Remote Access failed to apply server specific settings. |
| OTP ISAPI extension state | The OTP authentication ISAPI extension has stopped, and DirectAccess cannot function as expected. |
| RADIUS server availability | A connection to the RADIUS server configured for OTP authentication cannot be established. |
| RADIUS server connectivity | A connection cannot be established to any of the RADIUS servers from Remote Access server. |
| CA server availability | A connection cannot be established to CA server used for OTP authentication. |
| CA server configuration state | CA server used for OTP authentication is configured incorrectly. |
| CA server reachability | A connection cannot be established to any of the CA servers from Remote Access server. |
| Otp Certificate template availability | Certificate template configured for OTP authentication cannot be reached or is configured incorrectly. |
| Otp Certificate template configuration | Certificate template used for OTP authentication is configured incorrectly. |
| The OTP signing certificate is missing or configured incorrectly. | An OTP signing certificate cannot be located on the Remote Access server. |
| OTP ISAPI extension incorrectly configured | The OTP authentication ISAPI extension is not configured correctly, and DirectAccess cannot function as expected. |
| The OTP signing certificate is missing or configured incorrectly. | An OTP signing certificate cannot be located on the Remote Access server. |
| NLB driver state | Services required for server to work as expected in the cluster are not running. Remote clients will not be able to connect to the internal network via this server. |
| NLB service state | Services required for server to work as expected in the cluster are not running. Remote clients will not be able to connect to the internal network via this server. |
| NLB state | The cluster state on this server is stopped, suspended, draining or converging. |

### RRAS Monitoring

The Remote Access Management Pack manages the logical parts of a RRAS server that an operator or administrator is interested in monitoring, configuring, or reporting on. Each of the following components is critical to the VPN infrastructure:

| Component | Component Description |
| --- | --- |
| RAS client | You can create dial-up and broadband remote access connections to reach remote computers. With the PPTP, L2TP/IPsec, SSTP, and IKEv2 protocols, which are automatically installed on your computer, you can securely access resources on a network by connecting to a remote access server through the Internet or other network. The use of both private and public networks to create a network connection is called a virtual private network (VPN). |
| RAS connection establishment | Remote access involves establishing a dial-up or broadband connection with a remote access server. A dial-up client that connects to an RRAS can be any PPP client. The client must have installed a modem, an analog telephone line or other wide area network (WAN) connection, and remote access software. VPN clients that connect to RRAS must be able to send TCP/IP packets to the remote access server over the Internet. Therefore, a network adapter or a modem with an analog telephone line or other WAN connection to the Internet is required. |
| RAS connection termination | Remote access involves establishing a dial-up or broadband connection with a remote access server. A dial-up client that connects to an RRAS server can be any PPP client. The client must have installed a modem, an analog telephone line or other wide area network (WAN) connection, and remote access software. VPN clients that connect to RRAS must be able to send TCP/IP packets to the remote access server over the Internet. Therefore, a network adapter or a modem with an analog telephone line or other WAN connection to the Internet is required. |
| VPN NAP enforcement client configuration | A Network Access Protection (NAP) enforcement client is responsible for requesting access to a network, communicating a client computer's health status to the NAP server that is authorizing the network access, and communicating the connection status of the client computer to other components of the NAP client architecture. A NAP-capable client is a computer that has the NAP components installed and can verify its health state by sending a statement of health (SoH) to Network Policy Server (NPS). The remote access enforcement client enforces health policies when a client computer attempts to gain access to the network through a virtual private network (VPN) connection. |
| RRAS server | With RRAS, you can deploy VPN and dial-up remote access services, and multiprotocol LAN-to-LAN, LAN-to-WAN, VPN, and network address translation (NAT) routing services. |
| RAS connection | An RRAS server provides two different types of remote access connectivity: VPN and dial-up networking. VPN is the creation of secure, point-to-point connections across a private network or a public network, such as the Internet. A VPN client uses TCP/IP-based tunneling protocols to make a connection to a virtual interface on a VPN server. In dial-up networking, a remote access client makes a nonpermanent, dial-up phone or ISDN connection to a physical port on an RRAS server. In contrast to dial-up networking, VPN is always a logical, indirect connection between the VPN client and the VPN server over a public network, such as the Internet. |
| RASMAN service configuration | Connection Manager is a client dialer and connection software program. You can customize it by using the Connection Manager Administration Kit (CMAK) wizard to create a service profile. The Remote Access Connection Manager (RASMAN) service establishes the connection to the remote server. |
| RRAS audits | The Routing and Remote Access service has determined that RRAS audits generated an audit entry when a system event was executed successfully. These events confirm successful RRAS operations. |
| RRAS authentication and accounting | If a remote access server is configured for Windows authentication, the security features of Windows Server and Active Directory Domain Services (AD DS) are used to verify the credentials for authentication, and the dial-in properties of the user account are used to authorize the connection. If the remote access server is configured for RADIUS authentication, the connection request, including credentials, is forwarded to the RADIUS server for authentication and authorization. If the RADIUS server is a computer running Network Policy Server (NPS), NPS performs authentication against the credentials that are stored in the user account database, such as AD DS or the local Security Accounts Manager (SAM) database. NPS performs authorization using the dial-in properties of the user account and network policies that are configured in NPS. |
| RRAS computer certificate for EAP-TLS | When you use Extensible Authentication Protocol (EAP) with a strong EAP type, such as Transport Layer Security (TLS) with smart cards or certificates, the client and the server use certificates to verify their identities to each other. For successful authentication, certificates must meet requirements on the server and on the client. For information about computer certificates for EAP-TLS, see EAP Overview (http://go.microsoft.com/fwlink/?LinkId=164475) and Certificate Requirements for PEAP and EAP (http://go.microsoft.com/fwlink/?LinkId=164476) in NPS Help in the Windows Server Technical Library. |
| RRAS connection licenses | A client access license (CAL) is required for each client device or user that accesses a Windows Server operating system. Per-server connections are allocated on a first-come, first-served basis, and are limited to the number of CALs allocated to the server. A server that is over its licensed connection limit will not accept remote connections. |
| RRAS demand-dial connections | A demand-dial interface is a logical interface that represents a point-to-point connection. The point-to-point connection is based on a physical connection (such as two routers that are connected over an analog phone line that uses modems) or a logical connection (such as two routers that are connected over a VPN connection that uses the Internet). Demand-dial connections are on-demand (the point-to-point connection is only established when needed) or persistent (the point-to-point connection is established and then remains in a connected state). Demand-dial interfaces typically require an authentication process to become connected. The equipment required by a demand-dial interface is a port on a device. |
| RRAS DHCP Relay Agent (IPBOOTP) | The Dynamic Host Configuration Protocol (DHCP) Relay Agent component relays DHCP messages between DHCP clients and DHCP servers on different IP networks. The DHCP Relay Agent is compliant with RFC 1542, "Clarifications and Extensions for the Bootstrap Protocol." For each IP network segment that contains DHCP clients, a DHCP server or a computer acting as a DHCP Relay Agent is required. |
| RRAS DHCPv6 Relay Agent | The DHCPv6 Relay Agent relays DHCPv6 messages between DHCPv6 clients and DHCPv6 servers on different IPv6 networks. The DHCPv6 Relay Agent is compliant with RFC 3315. |
| RRAS hardware devices | RRAS uses network interface cards and modems to establish remote access connections. |
| RRAS IGMP | Internet Group Management Protocol (IGMP) maintains host group membership on a local subnet. Hosts use IGMP to communicate multicast group membership requests with their local multicast router. Routers receive the group membership requests and periodically send queries to determine which host groups are active or inactive on the local subnet. |
| RRAS IPCP negotiation | The VPN server must have IP addresses available to assign to the VPN server's virtual interface and to VPN clients during the IP Control Protocol (IPCP) negotiation phase of the connection process. The IP address that is assigned to the VPN client is assigned to the virtual interface of the VPN client. RRAS can be configured to use a DHCP server to obtain IP addresses or it can use a static pool of IP addresses to assign to remote access and demand-dial connections. |
| RRAS IPsec configuration | For L2TP-based VPN connections, a certificate infrastructure is required to issue computer certificates that are used to negotiate authentication for Internet Protocol security (IPsec). If the computer certificate that is required for IPsec is not available, the connection fails. |
| RRAS Multicast Group Manager | The Multicast Group Manager (MGM) application programming interface (API) enables developers to write multicast routing protocols that operate with routers running the Multicast Group Manager. When more than one multicast routing protocol is enabled on a router, the MGM coordinates operations between all routing protocols. The MGM informs each routing protocol when group membership changes occur, and when multicast data from a new source or destined to a new group is received. |
| RRAS multicast scope configuration | A multicast scope is a named range of IP multicast addresses that is expressed with an IP address and mask. After multicast scopes are configured, you can use them to create scope-based multicast boundaries in the properties of an IP routing interface. RRAS can forward multicast traffic in limited network configurations. The primary use of RRAS as a multicast router is to connect a subnet to a multicast-enabled intranet that contains routers running multicast routing protocols. To fully support efficient multicast forwarding on a multiple-router intranet, you must install multicast routers that run one or more multicast routing protocols. |
| RRAS NAP and Network Access Quarantine Control | Network Access Protection (NAP) provides a platform to help ensure that client computers on a private network meet administrator-defined requirements for system health. NAP enforcement occurs at the moment client computers attempt to access the network through network access servers, such as a VPN server running RRAS, or when client computers attempt to communicate with other network resources. Network Access Quarantine Control is similar in function to NAP VPN enforcement, but it provides added protection for remote access connections only. NAP provides protection for IPsec-based communications, 802.1X authenticated connections, VPN connections, DHCP configuration, and Terminal Services Gateway connections. |
| RRAS non-Microsoft DLLS | To successfully load a non-Microsoft dynamic-link library (DLL), the DLL must have the correct Windows system environment path and registry location. |
| RRAS other remote access server configurations | Successful remote access and routing connections require the correct configuration of firewall settings and IP routing protocols. |
| RRAS packet filter configuration | RRAS supports IP packet filtering, which specifies which type of traffic is allowed into and out of the router. The packet filtering feature is based on exceptions. You can set packet filters per interface and configure them to do one of the following: pass through all traffic except packets that are prohibited by filters or discard all traffic except packets that are allowed by filters. |
| RRAS PPP initialization | During connection initialization, Point-to-Point Protocol (PPP) uses Link Control Protocol (LCP) to negotiate link parameters, such as the maximum PPP frame size, the use of Multilink, and the use of a specific PPP authentication protocol. |
| RRAS registry configuration | Successful remote access and routing connections require the correct configuration of registry settings. |
| RRAS RIP for IP | RRAS supports Router Information Protocol (RIP) versions 1 and 2. RIP version 2 supports multicast announcements, simple password authentication, and more flexibility in subnetted and Classless InterDomain Routing (CIDR) environments. |
| RRAS routing interfaces | The RRAS server uses a routing interface to forward unicast IP and multicast IP packets. There are two types of routing interfaces: LAN interfaces and demand-dial interfaces. A LAN interface is a physical interface that typically represents a local area connection that uses local area networking technology such as Ethernet. A demand-dial interface is a logical interface that represents a point-to-point connection. The point-to-point connection is based on a physical connection (such as two routers that are connected over an analog phone line that uses modems) or a logical connection (such as two routers that are connected over a VPN connection that uses the Internet). |
| RRAS Secure Socket Tunneling Protocol | Secure Socket Tunneling Protocol (SSTP) is a VPN tunneling protocol with features that allow traffic to pass through firewalls that block PPTP and L2TP/IPsec traffic. SSTP provides a mechanism to encapsulate Point-to-Point Protocol (PPP) traffic over the Secure Sockets Layer (SSL) channel of the HTTPS protocol. The use of HTTPS means that traffic flows through TCP port 443, a port commonly used for Web access. |
| RRAS supporting modules | To successfully load supporting modules, the dynamic-link library (DLL) must have the correct Windows system environment path and registry location. |

#### VPN Monitors and Alarms

The RRAS Management Pack includes monitors and alarms to notify the administrator of some erroneous conditions. The following table outlines these monitors:

| Monitor | Description |
| --- | --- |
| Hardware device error | The connection attempt failed because the device that is connected to the port is not responding. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Protocol initialization failure | Internet Group Management Protocol version 2 (IGMPv2) encountered an error during initialization. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Remote Access Connection Manager unexpected termination | The Remote Access Connection Manager (RASMAN) service was unexpectedly terminated. |
| Routing and Remote Access service unexpected termination | The Routing and Remote Access service was unexpectedly terminated. |
| Routing and Remote Access service monitor | The Routing and Remote Access service is not running. |
| Authentication or accounting failures | The Routing and Remote Access service encountered an error while performing authentication or accounting. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Configuration failures | Internet Group Management Protocol version 2 (IGMPv2) detected a configuration failure. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| IPsec related failures | The connection attempt failed because an IPsec-compatible certificate was not found. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Packet filter related failure | The Routing and Remote Access service encountered an error while configuring a packet filter. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| IPCP negotiation failure | The Routing and Remote Access service encountered an error while assigning an IP address to dial-in client(s) during IP Control Protocol (IPCP) negotiation. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Memory Allocation Monitor | The Routing and Remote Access service could not start or is not fully functional because of a memory allocation failure. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Memory allocation failure | The network address translation (NAT) protocol encountered a memory allocation failure. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| No more licenses monitor | A user was unable to connect to the RRAS server because the server exceeded its client license limit. This monitor must be manually reset by the administrator whenever it changes to a critical state. |
| Port open failures | The Routing and Remote Access service or the Remote Access Connection Manager service encountered an error while opening a port for remote access. This monitor must be manually reset by the administrator whenever it changes to a critical state. |

#### Performance Monitoring Scenarios

The RRAS Management Pack includes performance counters to let the administrator monitor the performance statistics for the RRAS server. The following table outlines these performance counters:

| Performance Counter | Description |
| --- | --- |
| Number of Active Connections | The total number of currently active remote access connections. |
| Total Errors | The total number of CRC, timeout, serial overrun, alignment, and buffer overrun errors for this connection. |
| Alignment Errors | The total number of alignment errors for this connection. Alignment errors occur when a byte received is different from the byte expected. |
| Buffer Overrun Errors | The total number of buffer overrun errors for this connection. Buffer overrun errors occur when the software cannot handle the rate at which data is received. |
| Bytes Received | The total number of bytes received for this connection. |
| Bytes Received/Sec | The number of bytes received per second. |
| Bytes Transmitted | The total number of bytes transmitted for this connection. |
| Bytes Transmitted/Sec | The number of bytes transmitted per second. |
| CRC Errors | The total number of cyclic redundancy check (CRC) Errors for this connection. CRC errors occur when the frame received contains erroneous data. |
| Frames Received | The total number of data frames received for this connection. |
| Frames Received/Sec | The number of frames received per second. |
| Frames Transmitted | The total number of data frames transmitted for this connection. |
| Frames Transmitted/Sec | The number of frames transmitted per second. |
| Percent Compression In | The compression ratio for bytes being received. |
| Percent Compression Out | The compression ratio for bytes being transmitted. |
| Serial Overrun Errors | The total number of serial overrun errors for this connection. Serial overrun errors occur when the hardware cannot handle the rate at which data is received. |
| Timeout Errors | The total number of timeout errors for this connection. Timeout errors occur when an expected frame is not received in time. |
| Total Errors/Sec | The total number of CRC, timeout, serial overrun, alignment, and buffer overrun errors per second. |

#### Event Monitoring Scenarios

The RRAS Management Pack includes event monitoring to let the administrator monitor the erroneous configuration or errors that occur during runtime on the RRAS server. The following table outlines these events:

Note

Parameters shown as %1, %2, and so on represent event details that are provided in the event message.

| Event | Description |
| --- | --- |
| Rasman - PPP initialization failure | The Remote Access Connection Manager service failed to start because it encountered an error while loading RASPPP.dll. |
| Ras connection failure | The user’s connection to the RRAS server was terminated. |
| Configuration failure | The Routing and Remote Access service failed to start because of an invalid configuration. |
| Interface Initialization failure | The Routing and Remote Access service failed to load or create an interface. |
| Some interfaces not working | The Routing and Remote Access service encountered an error while performing an operation on the interface. |
| Demand dial connection failed | The Routing and Remote Access service failed to establish the demand-dial connection. |
| Configuration change for authentication | The Routing and Remote Access service detected a change in configuration. This may affect the connectivity of already connected user(s). |
| Out of memory error | The Routing and Remote Access service could not start or is not fully functional because of memory allocation failure. |
| Authentication/Accounting failure | The Routing and Remote Access service encountered an error while performing authentication or accounting. |
| Loading RAS supporting modules failure | The Routing and Remote Access service could not start because it failed to load and initialize one of the RAS DLLs. |
| Hardware device error | The connection attempt failed because the device that is connected to the port is not responding. |
| Control Protocol initialization failure | The Routing and Remote Access service failed to start because it encountered an error in the PPP Link Control Protocol initialization. |
| No more licenses | A user was unable to connect to the RRAS server because the server exceeded its client license limit. |
| Rasman port open failure | The Routing and Remote Access service or the Remote Access Connection Manager service encountered an error while opening a port for remote access. |
| Rasman Service initialization failure | The Routing and Remote Access service could not start because of an initialization failure. |
| Multicast failure | The Routing and Remote Access service encountered a problem in multicasting. |
| Rasman service init error | The Remote Access Connection Manager service failed to start due to initialization failure. |
| RemoteAccess - PPP initialization failure | The Routing and Remote Access service failed to start because it encountered an error in the initialization of the Point-to-Point Protocol (PPP). |
| The service failed to start or terminated unexpectedly | The Routing and Remote Access service failed to start. |
| IPCP negotiation failure | The Routing and Remote Access service encountered an error assigning an IP address to dial-in clients during IP Control Protocol (IPCP) negotiation. |
| Loading 3rd Party DLL failure | The Routing and Remote Access service failed to start because it encountered an error while loading a vendor’s administration or security DLL. |
| Registry operation failure | The Routing and Remote Access service could not start because it could not access one or more required registry values. |
| IPsec related failures | The connection attempt failed because RRAS could not locate a suitable IPsec computer certificate. |
| External error | The Routing and Remote Access service encountered an error while trying to revert impersonation. |
| Packet filter related failure | The Routing and Remote Access service encountered an error while configuring a packet filter. |
| Discarded packet from peer | Internet Group Management Protocol version 2 (IGMPv2) discarded one or more packets from the peer router. |
| Protocol initialization failure | Internet Group Management Protocol version 2 (IGMPv2) encountered an error during initialization. |
| Socket operation failure | Internet Group Management Protocol version 2 (IGMPv2) encountered an error in socket operation. |
| Multicast join failure | Internet Group Management Protocol version 2 (IGMPv2) could not join to the multicast group. |
| Router manager's entry point to protocol failures | Internet Group Management Protocol version 2 (IGMPv2) encountered an error in a callback function to the router manager. |
| Configuration failure | Internet Group Management Protocol version 2 (IGMPv2) detected a configuration failure. |
| Issues with IGMP configured as RAS client | Internet Group Management Protocol version 2 (IGMPv2) encountered an error while connecting or disconnecting RAS client. |
| MGM operation failure | Internet Group Management Protocol version 2 (IGMPv2) encountered an error while registering with Multicast Group Manager (MGM). |
| RTM routes addition failure | Routing Information Protocol version 2 (RIPv2) failed to add routes to the Routing Table Manager (RTM). |
| Route ignored | Routing Information Protocol version 2 (RIPv2) ignored one or more routes advertised by a neighbor. |
| Socket operation failure | Routing Information Protocol version 2 (RIPv2) encountered an error in a socket operation. |
| Sending packets to peer failed | Routing Information Protocol version 2 (RIPv2) failed to send packets to the peer router. |
| Router manager's entry point to protocol failed | Routing Information Protocol version 2 (RIPv2) encountered an error in a callback function to the router manager. |
| External failure | The Routing Information Protocol version 2 (RIPv2) encountered an external error. |
| Protocol Initialization failure | Routing Information Protocol version 2 (RIPv2) encountered an error during initialization. |
| Discarded packet from peer | The Routing Information Protocol version 2 (RIPv2) discarded one or more packets from the peer router. |
| DHCP allocator failure | The DHCP allocator component of NAT encountered an error. |
| DNS proxy failure | The DNS proxy agent component of NAT encountered an error. |
| Packet discarded | The DHCP allocator component of NAT discarded a packet from client. |
| Socket operation failure | One of the components of the NAT encountered an error in a socket operation. |
| NAT failure | The network address translation (NAT) protocol encountered a configuration error. |
| Memory allocation failure | The network address translation (NAT) protocol encountered a memory allocation failure. |
| Discarded packet from peer | The DHCP Relay Agent discarded one or more packets from the peer. |
| DHCP relay failure | The DHCP Relay Agent encountered an error relaying a DHCP request or reply. |
| Router manager's entry point to protocol failed | The DHCP Relay Agent encountered an error in a callback function to the router manager. |
| Socket operation failure | The DHCP Relay Agent (IPBOOTP) encountered an error in socket operation. |
| Protocol initialization failure | The DHCP Relay Agent (IPBOOTP) encountered an error during initialization. |
| Routing protocol's entry point to MGM failed | Multicast Group Manager encountered an error during routing protocol registration or while enabling a routing protocol on an interface. |
| Routing protocol registration failure | The routing protocol registration with Multicast Group Manager failed. |
| Router manager's entry point to MGM failed | Multicast Group Manager (MGM) encountered an error in a callback function to the router manager. |
| Initialization failure | The Multicast Group Manager (MGM) encountered an error during initialization. |
| Unable to process MOBIKE update | Unable to process MOBIKE update for connection named %2. The error code returned is %3. |
| Disabling PPP AUTH on port | Disabling PPP AUTH for %2\\%3 on port %4. |
| SSTP client certificate missing | The certificate that is used for Secure Socket Tunneling Protocol (SSTP) is missing. You should configure a new certificate for SSTP or use default configuration. |
| SSTP wrong certificate configuration | The certificate hash that is used for Secure Socket Tunneling Protocol (SSTP) %1 is different than the certificate bound %2 to the Web listener (HTTP.sys). Configure SSTP to use the default certificate or the certificate that is bound to SSL. You can configure Web server applications to use the same certificate that is used by SSTP. |
| SSTP cookie add failure | Secure Socket Tunneling Protocol (SSTP) service could not configure the VPN server-specific cookies. |
| No network protocols were successfully negotiated | The user %2 connected to port %3 has been disconnected because no network protocols were successfully negotiated. |
| PPP Error on Port | The following error occurred in the Point-to-Point Protocol module on port: %2, Username: %3. %4. |
| CallBack Failure | The remote access server’s attempt to callback user %2 on port %3 at %4 failed because of the following error: %5. |
| Cannot receive initial data on port | Cannot receive initial data on port %2 because of the following error: %3 The user has been disconnected. |
| License Limit Exceeded | A user was unable to connect on a port. No more connections can be made to this remote computer because the computer has exceeded its client license limit. |

#### Tasks

After you import the RRAS Management Pack, a number of tasks are available in the Operations Manager Operations console. The following table describes these tasks:

| Task Name | Description |
| --- | --- |
| Computer Management | This task opens the Computer Management snap-in. |
| Event Viewer | This task opens the Windows Event Viewer. |
| Ping | This task pings the computer name of the selected computer. |
| Remote Desktop | This task opens a Remote Desktop session to the selected computer. |